Shelby Landen
ADGP 215

I.0: Requirements Documentation

I.1: Description of the Problem
Name: Physics Environment
Problem Statement: Implement a softbody physics simulation in the form of cloth.
Problem Specification:

I.2: Input Information

I.3: Output Information
The program will simulate a cloth reacting to forces such as gravity and wind.

I.4: User Interface Information
The user will adjust sliders in-game to adjust the parameters for the cloth simulation.

II.0: Design Documentation
II.1: System Architecture Description
The system consists of three classes. The main class, which will be attached to the object to simulate, is named SCloth. The other two, SParticle and Spring, are used by SCloth.

II.2: Information about the functions

File: SParticle.cs
Class: SParticle
Data Members

Name: position
Description: 3D location of the particle node

Name: velocity
Description: Represents a speed in a certain direction.

Name: acceleration
Description: The rate of change of velocity.

Name: mass
Description: Represents the resistance to forces.

Name: force
Description: A displacement direction.

Name: anchor
Description: Whether the particle node is fixed in a static position or not.

Name: animated
Description: Whether the particle node is in a movable state.

File: Spring.cs
Class: Spring
Data Members:

Name: SpringType
Description: an enum of spring types that will affect the spring constants

Name: spring
Description:

Name: damp
Description:

Name: restLength
Description:

Name: p1
Description: The first particle node in the spring

Name: p2
Description: The second particle node in the spring

Function: ComputeForce
Parameters: n/a
Description:
1) First calculates the spring force with the formula: F = -k*d
Where F is the force, k is the spring constant, and d is the rest length - the distance between node1 and node2.
2) After the spring force is calculated, calculate the damper force. First, take the dot between the normalized distance between node1 and node2, and the node1 velocity.
Take the dot between the normalized distance between node1 and node2, and the node2 velocity. Then the damper force is calculated with the formula: F = -bv
where F is the force, b is the damping constant, and v is node1.velocity - node2.velocity. This force is added to the spring force.
3) Two new forces are calculated from the above.
a) force1 = (spring force + damper force) * the normalized distance between node1 and node2.
b) force2 = the negative force1.
4) Force1 is applied to node1 and force2 is applied to node2 to create a spring.

File: SCloth.cs
Class: SCloth
Data Members:

Name: divisions
Description: Number of times to subdivide the grid

Name: cols
Description: Number of columns in the grid

Name: rows
Description: Number of rows in the grid

Name: setAnchorsMode
Description: When this is true, anchors can be set.

Name: stiffness
Description: How stiff the cloth will be

Name: dampening
Description: The dampening constant to apply to the springs

Name: restLength
Description: The length of the springs at which they rest.

Name: constMass
Description: the mass constant for each particle.

Name: particles
Description: The array of particle nodes

Name: springs
Description: The list of springs

Name: gravity
Description: The force of gravity that will be used in force calculation.

III.0: Implementation Documentation
III.1 Program Code

#File: SCloth.cs
using UnityEngine;
using UnityEngine.UI;
using UnityEditor;
using System.Collections.Generic;

public class SCloth : MonoBehaviour
{
    public int divisions = 0;
    public int cols = 2;
    public int rows = 2;
    int width = 1;
    int height = 1;

    public float stiffness = 1;
    public float dampening = 1;
    public float restLength = 1;
    public float constMass = 0.5f;

    public float drag = 0.5f;
    public float density = 1f;

    public Slider stiffnessSlider, damperSlider, restLengthSlider;//, massSlider;
    public Slider windSliderX, windSliderY, windSliderZ;

    public SParticle[] particles;
    public List<Spring> springs = new List<Spring>();
    public List<LineRenderer> springsLines = new List<LineRenderer>();
    public List<Triangle> triangles = new List<Triangle>();

    public GameObject line;
    public GameObject particleGizmo;

    Vector3 gravity = new Vector3(0, -9.8f, 0);
    public Vector3 airVelocity = new Vector3(1, 1, -5);

    public float structuralSpringConst;
    public float structuralSpringRestLength;
    public float structuralDampConst;

    public float shearSpringConst;
    public float shearSpringRestLength;
    public float shearDampConst;

    public float bendSpringConst;
    public float bendSpringRestLength;
    public float bendDampConst;
    public GameObject cutter;

    void Awake()
    {
        //instantiate particle gizmo
        if (particleGizmo == null)
        {
        particleGizmo = new GameObject();
        Debug.Log("particleGizmo not set");
        }
        particleGizmo = Instantiate(particleGizmo) as GameObject;
        particleGizmo.name = "NodeMesh";
        particleGizmo.transform.parent = transform;
        particleGizmo.SetActive(false);

        //instantiate cutter
        cutter = Instantiate(cutter) as GameObject;
        cutter.name = "Cutter";
        cutter.transform.parent = transform;
        Vector3 offscreen = new Vector3(-100, 0, 0);
        offscreen = Camera.main.ScreenToWorldPoint(offscreen);
        cutter.transform.position = offscreen;

        //determine number of grid points after subdividing
        Subdivide(divisions);
        int totalPoints = rows * cols;
        particles = new SParticle[totalPoints];

        //set grid points
        int iter = 0;
        for (int i = 0; i < rows; ++i)
        {
        for (int j = 0; j < cols; ++j)
        {
        //create particles
        SParticle p = new SParticle();

        p.position = new Vector3(transform.position.x + j,	transform.position.y + i, transform.position.z + 0);
        p.mass = constMass;
        p.velocity = Vector3.zero;
        particles[iter] = p;

        ///create springs///
        //horizontal springs
        if (j != 0)
        {
        Spring s = new Spring();
        s.springType = SpringType.structural;
        s.spring = structuralSpringConst;
        s.damp = structuralDampConst;
        s.restLength = structuralSpringRestLength;

        s.p1 = particles[i * cols + j - 1];
        s.p2 = particles[i * cols + j];
        springs.Add(s);
        }

        ////horizontal bend springs
        //if (j != 0)
        //{
        // Spring s = new Spring();
        // s.springType = SpringType.bend;
        // s.spring = stiffness;
        // s.damp = dampening;
        // s.restLength = this.restLength;

        // s.p1 = particles[i * cols + j - 1];
        // s.p2 = particles[i * cols + j];
        // springs.Add(s);
        //}

        //vertical springs
        if (i != 0)
        {
        Spring s = new Spring();
        s.springType = SpringType.structural;
        s.spring = structuralSpringConst;
        s.damp = structuralDampConst;
        s.restLength = structuralSpringRestLength;

        s.p1 = particles[(i - 1) * cols + j];
        s.p2 = particles[i * cols + j];
        springs.Add(s);
        }

        ////vertical bend springs
        //if (i != 0)
        //{
        // Spring s = new Spring();
        // s.springType = SpringType.bend;
        // s.spring = stiffness;
        // s.damp = dampening;
        // s.restLength = this.restLength;

        // s.p1 = particles[(i - 1) * cols + j];
        // s.p2 = particles[i * cols + j];
        // springs.Add(s);
        //}

        //diagonal up right springs
        if (i != 0 && j != 0)
        {
        Spring s = new Spring();
        s.springType = SpringType.shear;
        s.spring = shearSpringConst;
        s.damp = shearDampConst;
        s.restLength = shearSpringRestLength;

        s.p1 = particles[(i - 1) * cols + j - 1];
        s.p2 = particles[i * cols + j];
        springs.Add(s);
        }

        //diagonal up left springs
        if (i != 0 && j != cols - 1)
        {
        Spring s = new Spring();
        s.springType = SpringType.shear;
        s.spring = shearSpringConst;
        s.damp = shearDampConst;
        s.restLength = shearSpringRestLength;

        s.p1 = particles[(i - 1) * cols + j + 1];
        s.p2 = particles[i * cols + j];
        springs.Add(s);
        }

        iter++;
        }

        }

        //create triangles
        for (int i = 0; i < totalPoints; ++i)
        {
        if ((i < totalPoints - rows) && ((i % rows) != (rows - 1)))
        {
        Triangle t1 = new Triangle();
        Triangle t2 = new Triangle();
        Triangle t3 = new Triangle();
        Triangle t4 = new Triangle();
        //NW, NE, SW
        t1.p1 = particles[i];
        t1.p2 = particles[i + 1];
        t1.p3 = particles[i + cols];

        //NW, NE, SE
        t2.p1 = particles[i];
        t2.p2 = particles[i + 1];
        t2.p3 = particles[i + cols + 1];

        //NE, SW, SE
        t3.p1 = particles[i + 1];
        t3.p2 = particles[i + cols];
        t3.p3 = particles[i + cols + 1];

        //NW, SW, SE
        t4.p1 = particles[i];
        t4.p2 = particles[i + cols];
        t4.p3 = particles[i + cols + 1];

        triangles.Add(t1);
        triangles.Add(t2);
        triangles.Add(t3);
        triangles.Add(t4);
        }

        }

        //set start anchor points
        particles[(totalPoints - cols)].anchor = true;
        particles[totalPoints - 1].anchor = true;
    }

    void Start()
    {
        //set UI elements
        stiffnessSlider.value = stiffness;
        damperSlider.value = dampening;
        restLengthSlider.value = restLength;

        windSliderX.value = airVelocity.x;
        windSliderY.value = airVelocity.y;
        windSliderZ.value = airVelocity.z;
        //massSlider.value = constMass;

        //make render lines
        int count = 0;
        GameObject sparent = new GameObject();
        sparent.name = "Springs";
        foreach (Spring s in springs)
        {
        GameObject g = Instantiate(line);
        g.name = "Spring " + count.ToString();
        g.transform.SetParent(sparent.transform);
        LineRenderer l = g.GetComponent<LineRenderer>();
        l.SetPosition(0, s.p1.position);
        l.SetPosition(1, s.p2.position);
        springsLines.Add(l);
        count++;
        }
    }

    void OnGUI()
    {
        stiffness = stiffnessSlider.value;
        dampening = damperSlider.value;
        restLength = restLengthSlider.value;

        airVelocity.x = windSliderX.value;
        airVelocity.y = windSliderY.value;
        airVelocity.z = windSliderZ.value;
        //constMass = massSlider.value;
    }

    void FixedUpdate()
    {
        bool gizmoActive = particleGizmo.activeSelf;
        Vector3 mousePos = new Vector3(Input.mousePosition.x, Input.mousePosition.y, 0);

        //compute particle forces
        foreach (SParticle p in particles)
        p.force = p.mass * gravity;

        //tearing
        if (Input.GetMouseButton(1))
        {
        Vector3 screenPoint = Camera.main.WorldToScreenPoint	(cutter.transform.position);
        Vector3 mouseWorldPos = mousePos;
        mouseWorldPos.z = screenPoint.z;
        mouseWorldPos = Camera.main.ScreenToWorldPoint(mouseWorldPos);
        cutter.transform.position = mouseWorldPos;
        }

        //compute spring forces
        int e = 0;
        foreach (Spring s in springs)
        {
        switch (s.springType)
        {
        case SpringType.structural:
        s.spring = structuralSpringConst * stiffness;
        s.damp = structuralDampConst * dampening;
        s.restLength = structuralSpringRestLength * this.restLength;
        break;
        case SpringType.shear:
        s.spring = shearSpringConst * stiffness;
        s.damp = shearDampConst * dampening;
        s.restLength = shearSpringRestLength * this.restLength;
        break;
        }

        springsLines[e].SetPosition(0, s.p1.position);
        springsLines[e].SetPosition(1, s.p2.position);
        s.ComputeForce();
        e++;
        }

        //compute aerodynamic forces
        foreach (Triangle t in triangles)
        {
        //get the average velocity of the triangle points
        Vector3 velocity =(t.p1.velocity + t.p2.velocity + t.p3.velocity) / 3;
        //subtract the air velocity
        velocity -= airVelocity;

        Vector3 crossAB = Vector3.Cross((t.p2.position - t.p1.position),	(t.p3.position - t.p1.position));
        Vector3 normal = crossAB / Vector3.Magnitude(crossAB);

        //what is this?
        Vector3 aeroForce = -0.5f * drag * density * ((0.5f * Vector3.Dot	(velocity, normal) * velocity.magnitude) /	crossAB.magnitude) * crossAB;

        aeroForce /= 3f;

        t.p1.force += aeroForce;
        t.p2.force += aeroForce;
        t.p3.force += aeroForce;
        }

        //integrate motion and input checks
        for (int i = 0; i < particles.Length; ++i)
        {
        //convert the position of the particle to screen space
        Vector3 screenPoint = Camera.main.WorldToScreenPoint(particles[i].
position);
        //set the mouse position depth to the same as the particle position depth in screen coords
        mousePos.z = screenPoint.z;
        //get the distance squared to avoid the square root as it's not needed for this purpose
        float distanceSqrd = Vector3.SqrMagnitude(screenPoint - mousePos);

        //square the right hand side and do the distance check
        if (distanceSqrd < 4f * 4f)
        {
        particleGizmo.SetActive(true);
        particleGizmo.transform.position = particles[i].position;

        if (Input.GetMouseButton(0) && particles[i].animated != true)
        {
        particles[i].animated = true;
        }

        }
        else if (gizmoActive && !Input.GetMouseButton(0))
        {
        particleGizmo.SetActive(false);
        gizmoActive = false;
        }

        //dragging
        if (Input.GetMouseButton(0) && particles[i].animated == true)
        {
        Vector3 direction;
        direction = Camera.main.ScreenToWorldPoint(mousePos -	screenPoint);
        Vector3 newMousePos = new Vector3(mousePos.x, mousePos.y,	screenPoint.z);
        //particles[i].position = Camera.main.ScreenToWorldPoint	(newMousePos);
        particles[i].force += (Camera.main.ScreenToWorldPoint(newMousePos)	- particles[i].position) * 800;
        }

        //set the particle to not being moved while the mouse button	//is no longer being held down
        if (!Input.GetMouseButton(0))
        particles[i].animated = false;

        //anchoring
        if (Input.GetKeyDown(KeyCode.A) && particles[i].animated ||
        Input.GetKeyDown(KeyCode.A) && distanceSqrd < 4f * 4f )
        {
        if (particles[i].anchor == true)
        particles[i].anchor = false;
        else
        particles[i].anchor = true;
        }

        //integrate motion (cont.)
        if (particles[i].anchor == false)
        {
        Vector3 acceleration = particles[i].force / particles[i].mass;
        particles[i].velocity += acceleration * Time.fixedDeltaTime;
        particles[i].position += particles[i].velocity *	Time.fixedDeltaTime;
        }

        }
        gizmoActive = particleGizmo.activeSelf;

    }

    void Subdivide(int numDivs)
    {
        for (int i = 0; i < numDivs; ++i)
        {
        rows = (rows * 2) - 1;
        cols = (cols * 2) - 1;
        }
    }

}

#File: SParticle.cs
using UnityEngine;
using System.Collections;

public class SParticle
{
    public Vector3 position;
    public Vector3 velocity;
    public Vector3 acceleration;
    public float mass;
    public Vector3 force;
    public bool anchor = false;
    public bool animated = false;
}

#File: Spring.cs
using UnityEngine;

public enum SpringType { structural, shear, bend };
public class Spring
{
    public SpringType springType; //type of spring
    public float spring; // stiffness
    public float damp; // damper
    public float restLength; // rest length
    public SParticle p1, p2;

    public void ComputeForce()
    {
        //get the distance between the particle nodes to get the direction
        Vector3 dist = p2.position - p1.position;
        float force;

        // calculate the spring force
        force = -spring * (restLength - Vector3.Distance(p1.position,	p2.position));

        //calculate the damper force
        float p1Vel = Vector3.Dot(dist.normalized, p1.velocity);
        float p2Vel = Vector3.Dot(dist.normalized, p2.velocity);

        //append the damper force to the spring force
        force += (-damp * (p1Vel - p2Vel));

        //apply the force to particle 1 toward particle 2
        Vector3 force1 = force * dist.normalized;
        //apply the opposite reaction to the particle 1 force
        Vector3 force2 = -force1;

        p1.force += force1;
        p2.force += force2;
    }
}

#File: Game.cs
using UnityEngine;
using System.Collections;
using UnityEngine.UI;

public class Game : MonoBehaviour
{
    public Button reset, exit;
    SCloth clothProgram;

    void Awake()
    {
        clothProgram = FindObjectOfType<SCloth>();
    }

void OnGUI()
    {
        if(exit)
        {
        Application.Quit();
        }
        if (reset)
        {
        clothProgram.InitCloth();
        }
    }
}

IV.0: Verification and Validation Documentation
IV.1: Test Plan

IV.2: Operating Directions

The application has two areas of parameters that can be manipulated.
Wind:
X-Axis: This slider changes the horizontal magnitude of the wind.
Y-Axis: This slider changes the vertical magnitude of the wind.
Z-Axis: This slider changes the depth magnitude of the wind.
Cloth:
Stiffness: This slider changes how stiff the cloth should be.
Dampening: This slider changes how much the force dampens throughout the cloth.

Apart from the sliders, there are also input keys for further interactability.
Keys:
Mouse Button 1: Hold this button down over a cloth node to drag it around
Mouse Button 2: Hold this button down to begin cutting the cloth
 A: Press this button to anchor a cloth node